## Slide 1
  Developments of auxiliary chemical geothermometers applied to the Los Humeros and Acoculco geothermal fields (Mexico)
Bernard Sanjuan, Frederick Gal (BRGM), Ruth Alfaro (Universidad Michoacana)
Potsdam, February 2020
  www.gemex-h2020.eu
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 727550 and the Mexican Energy Sustainability Fund CONACYT-SENER, project 2015-04-68074.

## Slide 2
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro
Main objectives of this study
The knowledge of the temperature of the deep geothermal fluids, rock permeability and water reservoir capacity are three key parameters for developing deep geothermal energy
Improve the reservoir temperature estimation in high-temperature deep volcanic reservoirs such as Los Humeros and Acoculco by developing auxiliary chemical geothermometers like Na-Li, Na-Rb, Na-Cs, K-Sr, K-Mn, K-Fe, K-F, K-W, and compare the estimated temperatures with those using:
classical water geothermometers (Na-K, Na-K-Ca, K-Mg, SiO2, δ18OH2O-SO4…)
numerical multicomponent geochemical modelling
gas geothermometers (CO2-CH4-H2S-H2, CO2-CH4-H2, CO2-CH4, H2-Ar, CO2-Ar…)
Validate these geothermometers on the fluids from the Los Humeros geothermal wells where deep temperatures were measured
Test these geothermometers on fluids collected from thermal springs in the Los Humeros and Acoculco geothermal areas

## Slide 3
Existing data
Literature review relative to the Los Humeros and Acoculco geothermal areas
Collection of geological logs, temperature, pressure and geochemical data relative to waters discharged from 16 deep wells, located in the Humeros geothermal field (CFE documents)
Collection of geochemical data (including B isotopes for 5 waters) from several deep wells in the Humeros geothermal field (from Arellano et al., 2003, JVGR, 124, 67-88; Bernard et al., Applied Geochemistry, 2011; Pinti et al., JVGR, 2017)
Collection of geochemical data of 39 waters collected from thermal springs in the Acoculco geothermal area (CFE report 34-86, Exploration Department, December 1986; Hernandez et al., 2009; Peifer et al., 2014)
Exploitation of these first data (only the auxiliary Na/Li geothermometer could be tested because no data for the other trace elements was found)
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 4
Water sampling and analyses
Collection of waters from 7 geothermal wells, 4 thermal springs and 3 natural lagoons (crater lakes) in the Los Humeros area and from 7 thermal springs in the Acoculco area from March 22 to 28, 2018, in collaboration with the Italian CNR Lelli’s team and Mexican teams (CFE, Ruth Alfaro)
Chemical and isotope analyses of these 21 water samples in the BRGM laboratories
Geochemical and geothermometric data treatment and interpretation
Acoculco area
Los Humeros area
Geothermal wells sampled in the Los Humeros area
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 5
Main chemical characteristics
TDS and pH values for thermal and geothermal waters range from 0.35 to 4 g/l and from 3.2 to 8.9, respectively
Different types of waters:
HCO3-Cl-Na type: Los Humeros geothermal waters, most of the thermal waters
SO4-HCO3-Na type: Los Azufres and Virgen del Carmen thermal springs
Ca-Na-HCO3 type: Quetzalapa and El Rincon thermal springs
Na-Cl type: Lagunas de Atexcac and Alchichica
Los Humeros geothermal wells
Los Humeros thermal springs
Los Azufres thermal springs
Other thermal springs
Lagunas
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 6
Origin of the waters
All the thermal waters have a meteoric origin (GMWL)
Some of them and especially, the Los Humeros geothermal waters, indicate an 18O enrichment, which suggests water-rock processes at high temperature and/or low water-rock ratios
The Los Azufres, Chignahuapan, El Rincon, Jicolapa, Quetzalapa and Tepeyahualco thermal waters could have similar water recharge areas than those of the Los Humeros geothermal waters
The meteoric origin of the thermal and geothermal waters is confirmed (low Cl concentrations and Cl/Br values different from that of seawater). Different Cl/Br values between the Los Humeros geothermal waters (1200-1700) and the other thermal waters (70-700)
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 7
Classical aqueous geothermometers
Classical geothermometers such as Silica-Qz, Na-K, Na-K-Ca, K-Ca, δ18OH2O-SO4, etc., give an estimation of reservoir temperature of 290 ± 30°C for the Los Humeros geothermal waters. This temperature is concordant with the presence of an upper liquid-dominated reservoir area, with neutral pH at 290-330°C, in augite and hornblende andesites, or in deeper basalts
Among the different Na-Li thermometric relationships existing in the literature, only the Na-Li auxiliary geothermometer defined for North-Icelandic HT basaltic geothermal dilute waters (Sanjuan et al., 2014) give concordant temperature values (320 ± 30°C). The Na-Cs auxiliary geothermometer defined by Sanjuan et al. ( 2016) also gives concordant reservoir temperature values (270 - 340°C)
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro
The classical Na-K-Mg ternary plot indicates that all the thermal waters are immature, having not reached full chemical equilibrium with the host rocks. Classical geothermometers such as Silica, K-Mg and K-Ca, based on fluid equilibration with chalcedony, muscovite, clinochlore, K-felspar and calcite, which can re-equilibrate relatively fast, as well as the δ18OH2O-SO4, and the auxiliary K-Sr and K-F geothermometers defined by Sanjuan et al. (2016), indicate subsurface temperature estimations, which vary from 60 to 100°C
260-320°C
60-100°C

## Slide 8
Water-rock interaction processes
The waters collected from Los Humeros wells and Los Azufres thermal springs (Acoculco) are very enriched in B relative to the other thermal springs. In the world, only some geothermal waters from New Zealand seem to have similar high B concentrations and B isotope signatures close to those of the Los Humeros geothermal waters (cf. Lu et al., 2014)
The B isotope signatures for the Los Humeros geothermal waters ranging from -2.52 to -0.74 ‰ are slightly lower than those obtained by Bernard et al. (2011) (from -1.7 to 0.3 ‰), and are in good agreement with B isotope fractionation between waters and illite minerals at about 300°C (Williams et al., GCA, 2001)
For Los Azufres and Jicolapa thermal springs, the B isotope signatures are lower (-6.79 and -4.42 ‰, respectively). For the Chignahuapan, Quetzalapa and Tepeyahualco thermal waters, these signatures are higher (-0.17, -1.20 and 8.55 ‰, respectively)
After Lu et al. (2014)
Los Humeros and Acoculco fields
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 9
Water-rock interaction processes
The Ca-HCO3 diagram confirms high water-calcium carbonate interaction processes for most of the thermal waters
The Sr isotope signatures of these waters suggest interaction processes with marine carbonate minerals (close to the Mesozoic seawater values) and consequently, with predominance of more superficial waters than those of the Los Humeros geothermal waters
The Sr isotope signatures indicate interaction processes with volcanic rocks (andesite, basalt) for the Los Humeros geothermal waters and for Los Azufres thermal waters (but with mixture of more superficial waters)
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 10
Water-rock interaction processes
It appears that the Na/K and Na/Li ratios, for numerous thermal waters, are close to those of the Los Humeros geothermal fluids
Associated with δ7Li values (4.7 to 6.5‰) and relatively high B contents, and some escapes of deep reservoir hot gases which reach the surface, these ratios suggest that small fluxes of deep waters, despite their low-permeability environment, could be able to preserve, more or less, their original Na/K and Na/Li ratios (and to a lesser extent, their Na/Rb and Na/Cs ratios), resulting from the temperature of their deep reservoir (about 300°C), even after significant mixing with cold waters and cooling, during their ascent up to the surface
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 11
Main conclusions
The classical Na-K-Mg ternary diagram and main geothermometers such as Na-K, Na-K-Ca, K-Ca and δ18OH2O-SO4 indicate that full chemical equilibrium conditions at about 290 ± 30°C are only attained for the Los Humeros geothermal waters. The Sr isotope signature of these waters (≈ 0.7043) suggests an interaction with reservoir volcanic rocks (basalt or andesite)
This temperature and isotopic signature are concordant with the presence of an upper liquid-dominated reservoir area, with neutral pH at 290-330°C, located in augite and hornblende andesites, or in deeper basalts
Among the different Na-Li geothermometric relationships existing in the literature, only the Na-Li auxiliary geothermometer defined for North-Icelandic HT basaltic geothermal dilute waters give concordant temperature values (320 ± 30°C). The Na-Cs auxiliary geothermometer defined in 2016 also gives concordant temperature values (270-340°C)
The Los Humeros geothermal waters, HCO3-Cl-Na type, with a meteoric origin, are characterized by low salinities (TDS ≤ 3.5 g/l), high silica contents (up to 930 mg/l) and very high B concentrations (up to 1800 mg/l)
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 12
Main conclusions
For all the thermal waters (predominantly HCO3-Cl-Na type):
meteoric origin like the Los Humeros geothermal waters, but with much lower Cl/Br mass ratios (70 to 700 instead of 1200 to 1700)
mainly constituted of superficial waters interacting with marine calcium carbonate minerals probably formed during the Mesozoic period
immature waters (no full chemical equilibrium with the host rocks). Classical geothermometers like Silica, K-Mg and K-Ca, which can re-equilibrate relatively fast, as well as the δ18OH2O-SO4, and the K-Sr and K-F geothermometers, indicate subsurface temperature estimations, varying from 60 to 100°C
However, the Na/K and Na/Li ratios (and to a lesser extent, the Na/Rb and Na/Cs ratios), for numerous thermal waters, are close to those of the Los Humeros geothermal fluids (corresponding at reservoir temperatures of about 300°C). Associated with δ7Li values and relatively high B contents, and some escapes of deep reservoir hot gases which reach the surface, these ratios suggest the presence of small fluxes of deep waters, despite the low-permeability environment, and perturbing processes during their ascent up to the surface
In such a context, these ratios may be useful tools for HT geothermal exploration in volcanic environments
Developments of auxiliary geothermometers (Los Humeros and Acoculco geothermal fields)
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro

## Slide 13
Acknowledgements
The content of this presentation reflects only the authors’ view. The Innovation and Networks Executive Agency (INEA) is not responsible for any use that may be made of the information it contains.
We acknowledge the Comisión Federal de Electricidad (CFE) for kindly providing support and advice and for granting access to their geothermal fields. Data has been kindly provided by CFE. We are particularly grateful to Oscar López Romero for his help in collecting fluid samples in the Los Humeros field. We would like to express our gratitude to Rafael Alfaro for his help in collecting waters from thermal springs located in the Los Humeros area.
We also acknowledge our Mexican colleagues for their help and collaboration, especially Aida Lopez Hernandez, scientific coordinator of the GEMEX project, for her constant and valuable support. We are also very grateful to Ernesto Bahena Palomares, who was our driver and guide during all our field campaign.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 727550 and the Mexican Energy Sustainability Fund CONACYT-SENER, project 2015-04-68074
Developments of geothermometers applied to the Los Humeros and Acoculco geothermal fields
Bernard Sanjuan, Frederick Gal, and Ruth Alfaro